## Slide 1
Progress Report on
K-GMT & KMTNet
Ho-Il KIM
2011.11. 08.
5th EACOA Kyoto

## Slide 2
KMTNet Project
Sciences
Main Science
Telescope
Detector
Filter Changer and Shutter
Wide-field Photometric Systems
Buildings
KMTNet Sites
Project Schedule
Contents
K-GMT Project
GMT : Off-Axis Primary #1
GMT1 Surface Maps
Primary Mirror Covers
1st Generation Instruments
Instrument Mounting
GMT : Preparation to PDR
Community-wide Science Promotion
Preparation for GMT era in KASI
K-GMT 2011 : Data Center
FSM prototype development
GMTNIRS
1. K-GMT in 2011
2. KMTNet in 2011
5th EACOA Kyoto

## Slide 3
K-GMT in 2011
Overview of K-GMT Project in 2011
5th EACOA

## Slide 4
K-GMT Project
Period : 2009 ~ 2018
Budget : USD74M + KRW16.9B
Project Goals :
Acquire 10% share of GMT
Science Promotion for GMT era
Engineering development in high-precision optics/optomechanics
- Fast Steering Secondary Mirror development
- GMT instrument development (GMTNIRS)
Overview of K-GMT Project in 2011
5th EACOA

## Slide 5
GMT : Off-Axis Primary #1
Overview of K-GMT Project in 2011
Development at SOML / Univ. Arizona
Fabrication finish in Nov. 2011
Most pacing item of GMT development
GMT PM#2 casting : Jan. 2012
GMT PM#3 casting : Feb. 2013
5th EACOA

## Slide 6
GMT#1 Surface Maps
Overview of K-GMT Project in 2011
June
August
71 nm
38 nm
September
5th EACOA

## Slide 7
Primary Mirror Covers
Overview of K-GMT Project in 2011
Mirror covers clear the beam – even for the center segment!
The only ELT having mirror covers
5th EACOA

## Slide 8
1st Generation Instruments
6 candidates : conceptual studies reviewed
2011. 9. 8. ~ 2011. 10. 7.
Instrument Development Advisory Panel organized
2-4 instruments will be selected before end of 2011
Overview of K-GMT Project in 2011
5th EACOA

## Slide 9
Overview of K-GMT Project in 2011
Name | Function | Remark
GMACS | Wide field multi-object optical spectrograph | Non AO
NIRMOS | NIR multi-object spectrograph | Non AO
GMTIFS | Integral-Field spectrograph | Non AO
GMTNIRS | High-Resolution NIR/MIR spectrograph | AO
GCLEF | High dispersion, high stability optical spectrograph | AO
TIGER | MIR Infrared imager | AO
1st Generation Instruments
5th EACOA

## Slide 10
Instrument Mounting
Overview of K-GMT Project in 2011
NIRMOS
GMACS
GMTIFS
GMTNIRS
TIGER
G-CLEF
5th EACOA

## Slide 11
GMT : Preparation to PDR
PDR plan : the end of 2012
Science case update will be completed soon or later
1st gen. instruments will be selected in this year
Conceptual design contract for major parts
Enclosure / facilities
Site preparation
Bearings / linear drives
Data Archives and data center
Overview of K-GMT Project in 2011
5th EACOA

## Slide 12
Community-wide Science Promotion
K-GMT Science & Instrument working group
15 members
- 10 professors from Universities + 5 KASI members
Internal activities
- Host international workshop
- Summer / winter school on GMT science cases
International collaboration
- Participate in science working group for 1st generation instrument candidates
- Working as panelists to review and select 1st generation instruments
- Participate in the science cases update work
Overview of K-GMT Project in 2011
5th EACOA

## Slide 13
Community-wide Science Promotion
New positions in KASI GMT group
KASI-Carnegie fellowship : one postdoc started works
Two more postdocs hired in 2011
Total 6 postdocs working in K-GMT group
Overview of K-GMT Project in 2011
5th EACOA
KASI endeavors to hire more and more young researchers

## Slide 14
Two research groups
GEMS0 : Star formation in the Galaxy
- Using AAT 3.9m telescope, planning UKIRT 4m
DREAM : Galaxy formation and evolution in cluster of galaxies
- Used CFHT 3.6m and Magellan 6.5m this year
Both groups collaborate actively with Universities
Overview of K-GMT Project in 2011
Preparation for GMT era in KASI
5th EACOA

## Slide 15
GMT Data Center Conceptual study
Need to consider how to deal with the data from various instruments
Need to prepare for mirror servers in partner institutions, especially for
Korea and Australia
International Collaboration
Members : Harvard CfA, KASI, ANU, AAL
Period : Sep. 2011 – Jun. 2012
Overview of K-GMT Project in 2011
K-GMT 2011 : Data Center
5th EACOA

## Slide 16
FSM : conventional secondary mirror for GMT
International and domestic collaboration
KASI-NOAO (design and development)
KASI-KRISS-GIST-IAE-SELAB
MRR : Sep. 22-23, 2011
TRR : Mar. 2012
Prototype Completion : End of 2012
Overview of K-GMT Project in 2011
FSM prototype development
5th EACOA

## Slide 17
KASI-UT Austin collaboration
A high resolution NIR spectrograph using Silicon Immersion Grating
Simultaneous observation in JHK – LM bands.
One of 1st GMT generation instrument candidates
Conceptual design review Oct. 3-4 : passed
Final selection in this year as a 1st generation instrument
Overview of K-GMT Project in 2011
GMTNIRS
5th EACOA

## Slide 18
Overview of K-GMT Project in 2011
GMTNIRS
M-band spectrograph shield
L-band spectrograph shield
JHK-band spectrograph Modules
Slit/OIWFS housing
LGS pickoff mirror
5th EACOA

## Slide 19
KMTNet in 2011
Overview of KMTNet Project in 2011
5th EACOA

## Slide 20
KMTNet Project
Period : 2009 ~ 2018
Budget : KRW30B(~USD26M)
Development of the KMTNet System
Korea Micro-lensing Telescope Network
Three Identical Observing Systems
Will be installed at CTIO in Chile, SAAO in South Africa, and
SSO in Australia by the middle of 2014
24-hours uninterrupted Monitoring of night sky at Southern Hemisphere
5th EACOA
Overview of KMTNet Project in 2011

## Slide 21
Sciences
Wide-field Photometric Monitoring
Search for Extra-solar Planets, especially, Earth-mass Planets
in the Habitable Zone, using the micro-lensing technique
Wide-field Photometric Surveys
Surveys of Transiting Planets and Variable Objects
Surveys of Clusters, Galaxies, SNs, Near-Earth Objects, etc.
5th EACOA
Overview of KMTNet Project in 2011

## Slide 22
Main Science
Detection of micro-Gravitational Lensing events
Monitoring the Galactic Bulge
Discovery of extra-solar planets
5th EACOA
Overview of KMTNet Project in 2011

## Slide 23
Telescope
Wide Field Optical Telescope
Primary Mirror with 1.6m Diameter
Prime Focus type Reflector
Equatorial Mount
FOV of 2o
Four Field Corrector Lenses
Delivered Image Quality of 1.0” FWHM under
0.75” seeing
5th EACOA
Overview of KMTNet Project in 2011

## Slide 24
Detector
Large-Format Mosaic CCD camera
Four e2v chips with 9k by 9k pixels
10x10 microns pixel
0.4”/pixel. 2x2 deg. sq. FOV
High Quantum Efficiency of ~90%
Cryogenic Cooling System
5th EACOA
Overview of KMTNet Project in 2011

## Slide 25
Filter Changer and Shutter
Cassette-Style Filter Changer
Four Spectral Filters with 310x310mm square
Johnson-Cousins BVRI and SDSS griz filter sets
Bonn-Style Shutter
Sliding Shutter with 325x325mm square Clear Aperture
5th EACOA
Overview of KMTNet Project in 2011

## Slide 26
Wide-field Photometric Systems
Telescope | Camera | FOV | Site | Target
PanSTARRS 4x1.8m | 1400M pixel CCD | 7.0 deg2 | Haleakala, USA | All sky survey
MOA 1.8m | 80M pixel CCD | 2.4 deg2 | Mt. John, New Zealand | Galactic Bulge
KMTNet 3x1.6m | 340M pixel CCD | 4.0 deg2 | CTIO – SAAO – SSO | Galactic Bulge
SkyMapper 1.35m | 268M pixel CCD | 5.7 deg2 | SSO, Australia | All sky survey
OGLE-IV 1.3m | 268M pixel CCD | 1.4 deg2 | LCO, Chile | Galactic Bulge
LCOGT 2x2.0m, 10x1.0m, 14x0.6m | 16M pixel CCD | 0.03 deg2 0.20 deg2 | Haleakala–Canary–CTIO–SAAO–SSO | Follow-Up Obs. Exoplanet, GRB
5th EACOA
Overview of KMTNet Project in 2011

## Slide 27
Wide-field Photometric Systems
Chart: 
| 0 | 1.6 | 2 | 6 | 10
계열 1 | 4
5th EACOA
Overview of KMTNet Project in 2011

## Slide 28
Buildings
Observing Dome
Ash Dome with 9.2m Diameter.
Air-Ventilation System
5th EACOA
Overview of KMTNet Project in 2011

## Slide 29
Buildings
Auxiliary Building
Control room
Computer room
Storage
5th EACOA
Overview of KMTNet Project in 2011

## Slide 30
KMTNet Sites
SAAO
SSO
CTIO
KASI
5th EACOA
Overview of KMTNet Project in 2011

## Slide 31
KMTNet Sites
CTIO
5th EACOA
Overview of KMTNet Project in 2011

## Slide 32
KMTNet Sites
SSO
5th EACOA
Overview of KMTNet Project in 2011

## Slide 33
KMTNet Sites
SAAO
5th EACOA
Overview of KMTNet Project in 2011

## Slide 34
Project Schedule
 | Development of the System | 
2009 | Concept Design of the Wide-Field Telescope and Mosaic Camera | 
Jul.2010 | Contract of the KMTNet Telescope | 
Mar.2011 | Final Design Completion of the Telescope | 
Jun.2011 | Contract of the KMTNet Camera & Telescope Manufacturing Start | 
Aug.2011 | Finish Polishing the First Primary Mirror | 
Dec.2011 | Final Design Completion of the Camera | 
Mid-2013 | First Light of the First System at CTIO in Chile | 
By Mid-2014 | First Light of the Second and Third Systems | 
5th EACOA
Overview of KMTNet Project in 2011

## Slide 35
Thank you!
Korea Giant Magellan Telescope
Korea Micro-lensing Telescope Network
5th EACOA